Drilling Unit «ТW125CA-A6» (Romania)

Year of construction: 2008

Capacity: 125 ton

Maximum drilling  depth and workover: Drilling-3000m, workover -5400m

Intended purpose: exploratory and production well-drilling, workover

Drilling method: rotatory drilling method with washing before bottomhole - rotor

Mechanics drives: mobile on chassis equipped with diesel Caterpiller

Mast: telescopic with hoist system and hydraulic hoisting  jack

Mud feed: by one triplex pump

Drilling unit: «ZJ 70LDB» (China)

Year of construction: 2011                                                                                                                           Capacity: 450 ton                                                                                                                                             Maximum drilling depth: 7000 m                                                                                                              Intended purpose: oil and gas exploratory and production well-drilling                                            Drilling method: rotatory drilling method with washing before bottomhole – rotor, turbine, top drive “Top-Drive”                                                                                                                                               Mechanics drive: combined (mechanical and electric)                                                                                                                                         Mast:  K-mast, sectional                                                                                                                                       Mud feed: by three triplex pumps

Drilling unit: «F320-3DHU-2А» (Romania)                                                                                                    Year of construction: 1988                                                                                                                               Capacity :320   ton                                                                                                                                                  Maximum drilling depth: 6000 m Intended purpose : exploratory and production well-drilling Drilling method: rotatory drilling method with washing before bottomhole - rotor, turbine                                                                                                               Mechanics drive: mechanical                                                                                                                             Mast:  А – mast, sectional                                                                                                                                                              Mud feed: by three triplex pumps

Drilling unit: «F400-4DH-U» (Romania)

Year of construction: 1989                                                                                                                          Capacity:400  ton Maximum drilling depth: 7000 m.                                                                        Purpose intended: exploratory and production well-drilling                                           Drilling method: rotatory with washing before bottomhole  – rotor, turbine                                                                                                                              Mechanics drive: mechanical                                                                                            Mast: А – mast, sectional                                                                                                      Mud feed: by two triplex and one two-cylinder pumps

Drilling unit: «Uralmash-3D – 86» (Russia)

Year of construction:  1988                                                                                                     Capacity:   320 ton                                                                                                             Maximum drilling depth:  5500 m                                                                                Intended purpose: exploratory and production well-drilling                                                   Drilling method: rotatory with washing before bottomhole – rotor, turbine                   Mechanics drive: mechanical                                                                                           Mast:  tower mast with flexible double lattice                                                                       Mud feed: by two triplex pumps

Drilling unit: «Р- 80» (Romania)

Year of construction:  1985                                                                                               Capacity: 80 ton                                                                                                             Maximum drilling depth and workover:  Drilling – 1000 m, workover – 3000 m.           Intended purpose:  exploratory and production well-drilling, workover                               Drilling method: rotatory with washing before bottomhole – rotor                                 Mechanics drive: mobile on chassis,

Mast:  telescopic with hoist system and hydraulic hoisting jack

Drilling unit «А – 50U» (Russia)

Year of construction: 1987                                                                                          Capacity:  50 ton                                                                                                          Maximum drilling depth and workover: drilling direction, workover- 1000 m               Intended purpose:  direction drilling, workover                                                               Drilling method: rotatory with washing before bottomhole  – rotor                               Mechanics drive: mobile, chassis on base of KRAZ                                                             Mast:  telescopic                                                                                                                   Mud feed: by cementing unit