Technical specification of

F-320-ЗDH-U-2а drilling rig.

- F-320-ЗDH-U-2а drilling rig.

Year of construction				- 1988

Construction number				- 411

Origin 	- Romania

Intended purpose –for oil-well and gas-well drilling up to 6000 m depth.

Location	                                                          -  Kazakhstan, Uralsk

maximum work hook load                          	- 320 ton.

number of threads in maneuvering system        	-10

number of  hook speeds			- 4

diameter of drill line        			- Ø 35 mm

number of speeds for rotary			-4 + 2 back

drift diameter of rotary  			- 698,5 mm (27 1/2")

maximum stand length   			- 27 m

height of working floor    			- 6700 mm

height up to rotary beams     			- 5500 mm

number of drill units        			- 3 units (СА-20) + 6 units (СА-25)

winch input power                                      		- 2000 HP

2.  МА-320 drill mast.

maximum hook load                       	 - 320 ton
height                                             		 - 48830 mm 
stand capacity of  27 m 5" length	 - 6210 m

5 1/2" 	 -5238 m

3. Racking platform basket travel cradle.

compressed air working pressure	- 7 bar.

air engine power               		-10 HP

air engine rotation           		-1400 rpm

reducer capacity              		- 4 kW

cradle travel speed                        	- 27 m/min

4. Racking platform with travelling cradle.

Platform mounting levels of the mast:

• level I                - 22670 mm

• level II               - 23670 mm

• level III              - 25670 mm

• level  IV              - 26670 mm

Stacking capacity with stands in 27 metre.

• stands in 5"	   - 6210 m

• stands in 51/2"  - 5258 m

5. Mast derrick support.

Maximum rotary load                    	   - 320 ton
maximum setbacks load                                 - 200 ton

maximum middle setback load from heavy rods plate -45 ton

uniformly acting whole working floor load  -1000 kg/m2

6. TF-38 draw works.

Type, mark, capacity                                                             – ТF-38, 2000 HP

Type of drive       	                                                     - diesel SА-20 – 3 units

Total drive power                                                                - 1986 kW

Type, mark of auxiliary brake                                        – hydraulic  brake FH-60"

Cooling system                                                                   – water

Diameter of main drum                                                     – 800

Type, diameter and line tensile strength                       – Ø 35mm.,75 ton

7. Rotary drive.

maximum drive power                    			- 600 HP

spool axis height from well floor level                     	 - 1425
maximum spool axis rotation                                     	- 300 rpm

maximum spool rope power at winding                  	- 3000 daN.
diameter of spool drum at winding                          	 - Ø 250 mm

maximum spool rope power at unwinding             	-12000 daN.
diameter of spool drum at unwinding                     	 -180 mm8.

8.MRL-275 rotary table.

Max. static table load              		 – 500 ton

Max. rotary table rotation  		– 300 rpm

Rotary drift diameter       		- 698,5 mm (27 1/2")

9. Dead line anchor drum ТА-40.

maximum dead anchor load                                	- 40 ton forc.

rope winding roll diameter 			- Ø 720 mm

10. Crown block  6х35-SG-500-U.

Maximum hook load                        		- 500 ton

external diameter of rope roll     		- Ø 1400 mm

diameter of rope roll groove bottom        	- Ø 1285 mm

number of rope rolls                   			- 6

diameter of rope				- Ø 35 mm

11. Travelling block  5х35-MS-400-U.

maximum working hook load                              	- 400 ton

hook travel					- 200 mm

number of rope rolls               			- 5

external diameter of rope roll     		- Ø 1400 mm

diameter of rope roll groove bottom        	- Ø 1285 mm

diameter of rope				- Ø 35 mm

12. Mud pump UNBT – 950,  No.1, No.2, No.3

type of pump – UNBT –950,  triplex

max. mud pump pressure – 32 mPa

max. mud pump capacity – 950 kW

type of  motor pump  – SА–25

number of motor pump units  – 6 units (2 units for each pump)

max. capacity of one unit – 600 kW

13. Swivel SN-400.

maximum static load                                    				- 400 ton 
dynamic load of main bearing at 100 rpm                                                  	- 210 ton
maximum working RPM                                                    			 - 300 rpm

diameter of stem flow area                                                			 - Ø 76 mm

maximum working pressure                                               			 - 300 kg/сm2

14. Compressor unit GPA-8-2\2ESC10V-0.

working fluid       						- compressed air

maximum working inlet tank  pressure                                         	-12 kg/сm2
compressor unit outlet pressure
(outlet tank)                                                          			 -10 kg/сm2
total tanks capacity 4x2000   	                       			 - 8000 litre (8m3)
type of electrical engine compressor unit            			- 2ЕС10ВО
number of electric engine compressors                               		 - 2

used compressor - type 2С10 with 4 cylinders form "V"
air consumption                                                       		- 5,4 m3 N/min ± 7%
nominal rotation                                            		 - 960 rpm

type of drive motor of compressor (АS1)MIV.З-280Мg 
motor power (synchronous rotation)           		- 55 kW/1000 rpm,
rated voltage                                                  		 - 380 V

15. Compressor SС-10.

rated rotation                                 - 900

min rotation        		- 400

max pressure 			-12 bar

working pressure                          - 10 bar

capacity                		- 5+7% m3/min

16. Driller’s panel

Pressure of pneumatic environment 	-10 bar.

Provides with all pneumatic operating control performed by foreman driller.

17. Power supply and diesel fuel storage

Is intended for  diesel fuel supply (by free fall) to rigs engines; consists of (19m3+4m3)

• daily tank capacity 	- 4m3

• reserve tank capacity	-19m3

• maximum  electric pump capacity

(at pressure 1,5 bar)	- 28 m3/hour

• average height of diesel fuel column              - 4,5 m
Reserve tank       	                                       - 28 m3.
Number of reserve tanks                                       - 3 pcs.

18. Sludge preparation, cleaning and circulation equipment.

1. Mud tanks.

а) mud tanks with total pumped volume 350 m3. Tanks divided in:

-    cleaning tank for 3 shale shakers,

-    desander and mud cleaner cleaning tank,

-    degasser,

-    one tank V=70m3  for mud preparation,

-    four active tanks with total capacity 280 m3.

b) one trip tank with capacity 18 m3, equipped with centrifugal pump.

2. Mud mixing equipment.

А)The unit is equipped with hydromixer  2    х    8"    for preparation and  weighting  of mud.

Hydromixer has:

-    gear ring for sack cutting

-    one feed hopper.

The hydromixer is equipped with  6" pipes with tank for mud preparation and works irrespective of drill pumps.

B) “SWACO” hydraulic hopper for mud preparation

Is equipped with  6" pipes with tank for mud preparation and works irrespective of drill pumps.

3. Shale shaker.

Number                                                                                                3                                                                                                                                                                                                      Mark and type                                                               “SWACO”ALS-II

4. Desander  - mud cleaner

Mark and type                                                                        6T4/ALS II “SWACO”                                                  Maximum flow rate, l/sec                                                     900 GPM

Number and size of cones                                                       12 pcs. 4”

Number of  feed pump                                                                           1

Mark  and type of feed pump                                                    II NE-80

Feed pump drive                                                                           electric

5. Centrifuge  518 «SWACO»

6. Vacuum degasser.

Capacity -   3180 l/min.

Degasser is equipped with:

-    vacuum electric pump, vacuum pump delivery rate – 275 m3/hour, maximum vacuum- 160mm.

7. Atmospheric degasser.

The unit is equipped with atmospheric degasser with air line 8" and blowing line with diameter 10".

8. Cellar pump.

Cellar mud is pumped with pneumatic pump.

9. Mud bucket.

Mud bucket is hanged on rope to the mast construction elements. Pipes range 3 1/2 х 5". Discharge hose is directed to cellar situated under  drill.

19. Manifold GMP-2IIH-1300 and GMP-2IIH-400.

Nominal diameter of pipeline - 4", working pressure - 350 bar., type of pipe stand - 4"- double, type of valves - RSDM-2",3",4". Vibration hose: nominal diameter - З1/!", length 3,5". Working pressure - 350 bar.

20. Automatic bit feed device (ДААС).

Maximum allowable rotations on input shaft - 12 rpm,

maximum allowable torque on input shift - 1600 daN.m

maximum travelling block load – 250 ton,

feed speed at drilling - 0-25 m/hour,

bit load correction  - 0-0,3 ton,

pulling speed at drill-stem saving  - 25 m/hour.

Kind of operation - pneumatic, centralised.

21.Make-up hydraulic tool.

Maximum load -14500 kg.

Nominal pressure -150 daN/сm2,

working pressure - 200 daN/сm2,

max. pressure - 240 daN/сm2

22. Derrickman evacuation device.

In case of danger provides with derrickman safety and his quick descent from derrickman working level to ground.

Vehicular load -100 kg, average slope of descent  30°.

Brake (mechanical with rolls on the rope) - manual.

23. Diesel generator 520 kW ( DGR  - 520/1000).

24. Diesel generator  «IVECO» - 520kW

25. Diesel generator  200kW (YaMZ-75117)

26. Power equipment.

Power equipment set includes:

а) three power plants with capacity 200, 520, 520 kW, supplying power to rig and all electric engines

b) power plant control panel;

c) three diesels of SА-20 type with capacity 662kW (each) for draw-works drive

d) six diesels SA-25 with capacity 600 kW(each) for three mud pumps drive UNBT – 950

27. Rig shelter.

Full length of shelter 28,534 m,

width 16,68 m,

truss span - 16,00 m,

covered surface 476 m2,

full weight 27,039 ton.

Circulating system shelter.

Full length of shelter 36,018 m,

width 16,68 m,

covers surface  600m2,

full weight -33,338 ton.

Shale shaker block shelter

Length 21,92m,

width 11,164 m,

truss span - 11,00m,

covered surface - 256 m2,

full weight- 16,69 ton.

28. Catwalk,

Height     1,07    m,

length of central catwalk     25,110     m,

width of rack 15,96m.

9 m length pipe laying ability:

29. Telemak NT-125 (hoisting telescopic crane)

Nominal load at Р=3m 12,5 ton.

Maximum load at Р=11,25m -1,8 ton.

Maximum hook height -13,4 m

30. Pneumatic slips PKR-560m)

Mechanical drive relief.

Load capacity- 320 ton.

Nominal diameter of taken pipe - 48 to 178 mm

Effective maximum length of drilling string 6500 m.

Number of sizes: slips with retrievable rams - 2,

hanged pipes -11.

Control  -  distance control from driller’s control panel

Intended for  drilling string hang during tripping operations.

31. Automatic drilling ton AKB-ЗМ2.

Range of performance:

for pipes with joints    108-216mm
for casing                        114-194mm

| No. | Name | Unit | Q-ty | Manufacturer |
| --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 |
| 1 | Drill mast МА-320 | pcs. | 1 | Romania 1988 |
| 2 | Drill mast hoisting system | set | 1 | Romania |
| 3 | Racking platform with travel cradle | set | 1 | Romania |
| 4 | Derrickman cradle traveling device | set | 1 | Romania |
| 5 | Derrick subbase | set | 1 | Romania |
| 6 | Draw-works TF-38 | pcs. | 1 | Romania |
| 7 | Hydraulic brake F-Х-60" | pcs. | 1 | Romania |
| 8 | Rotary chain drive | pcs. | 1 | Romania |
| 9 | Rotary table МRL - 275 | pcs. | 1 | Romania |
| 10 | Dead line anchor drum ТА-40 | pcs. | 1 | Romania |
| 11 | Crown block 6х35-GF-500U | pcs. | 1 | Romania |
| 12 | Traveling block 5х35-МS-400U | pcs. | 1 | Romania |
| 13 | Draw works drive engine SA-20 chain transmission I | pcs. | 1 | Romania 2005 |
| 14 | Draw works drive engine SA-20 chain transmission II | pcs. | 1 | Romania 2005 |
| 15 | Draw works drive engine SA-20 chain transmission III | pcs. | 1 | Romania 2005 |
| 16 | Mud pump UNBT – 950 | pcs. | 3 | Russia 2006/2008 |  |
| 17 | Motor pump UNBT – 950 (SА – 25) | pcs. | 6 | Russia 2006/2008 |  |
| 18 | Swivel SN-400 | pcs. | 1 | Romania |  |
| 19 | Air conditioning unit | set | 1 | Romania |  |
| 20 | Electrical engine compressor 2ЕС-10 | pcs. | 2 | Romania |  |
| 21 | I engine SА-2 transmission-driven Compressor 2С-10 | pcs. | 1 | Romania |  |
| 22 | Driller’s panel | pcs. | 1 | Romania |
| 23 | Fuel storage including: -Tank V=28m3 -Tank V= 19m3 -Daily tank V=4m3 Electric pump | set pcs. pcs. pcs. pcs. шт. | 3 1 1 1 | Romania Romania Romania Romania Romania |
| 24 | Mud mixing, cleaning and storage equipment ∑V = 478m3 including: - sandtrap tank V = 21,6m3 - shale shaker tank V = 50м3 - receiving tank V=5х70=350m3 - water tank V = 45m3 | set | 1 1 6 1 | Romania Romania Romania Romania Romania |
| 25 | Shale shaker “SWACO” ALS-11 | pcs. | 3 | Canada 2001 |
| 26 | Desander – mud cleaner “SWACO” ALS-11 | set | 1 | Canada 2001 |
| 27 | Centrifuge “SWACO” 5181 | pcs. | 1 | Canada 2001 |
| 28 | Hydraulic hopper «SWACO» | pcs. | 1 | Canada 2001 |
| 29 | Degasser | pcs. | 1 | Romania |
| 30 | Double pipe stand mudline manifold | set | 1 | Romania |
| 31 | Propeller blade mixer | pcs. | 14 | Romania |
| 32 | Automatic bit feed device | pcs. | 1 | Romania |
| 33 | Pipe tong 3 1/2 – 17 - 90KN | pcs. | 2 | Romania |
| 34 | Drill pipe fixing device | set | 1 | Romania |
| 35 | Air hoist LV-15 грузоподъёмностью 3000 кг. | pcs. | 1 | Russia |
| 36 | Derrickman evacuation device | set | 1 | Russia 2007 |
| 37 | Electric power plant supplying electrical units and lightning | set | 1 | Romania |
| 38 | Diesel-generator «IVECO» 520 kWт | pcs. | 1 | Italy 2007 |
| 39 | Diesel-generator 520 kW (DGR – 520/1000) | set | 1 | Russia 2005 |
| 40 | Diesel-generator 200 kW (YaMZ-75117) | set | 1 | Poland 2007 |
| 41 | Bulk material measuring and transport equipment | set | 1 | Romania |
| 42 | Hoisting crane NТ-125 «Тelemack» | pcs. | 2 | Romania |
| 43 | Pipe rack | pcs. | 8 | Romania |
| 44 | Central pipe bridge | pcs. | 1 | Romania |
| 45 | Skip bridge | pcs. | 1 | Romania |
| 46 | Setback | pcs. | 2 | Romania |
| 47 | Rig shelter | set | 1 | Romania |
| 48 | Ada mud measuring facility | pcs. | 1 | Romania |
| 49 | Automatic pneumatic power tong АKB-3 М2 | set | 1 | Russia |
| 50 | Swivel SN-400 | pcs. | 1 | Romania |
| 51 | Pneumatic slips for rotary PKR-560 | set | 1 | Russia |
| 52 | High pressure compressor KR-2-150 (for drill pump compensating device operation) | pcs. | 1 | Russia |
| 53 | BOP package OP 425 х210 | set | 1 | Russia 1987 |
| 54 | BOP package НDU- 13 5/8 x700 | set | 1 | Romania 1988 |
| 55 | BOP package PUG 350х350 | set | 1 | Russia 1988 |
| 56 | Boiler plant | set | 1 | Russia |
| 57 | Hydraulic wrench t «ECKEL» for casing | set | 1 | Canada 2001 |
| 58 | Hydraulic weight sensor GIV-6 | set | 1 | Russia |
| 59 | Drill measuring control “GEOTEC” complex : Hook weight Bit load Rotary torque Manifold pressure Pipe tong torque Working reception and trip tank mud level | set | 1 | Russia 2008 |
| 60 | heavyweight drillpipe Ø127mm., G-105 х 9,19 | metre | 6000 | France 2006 |
| 61 | drill collar Ø241mm. | metre | 60 | France 2007г. |
| 62 | drill collar Ø203mm. | metre | 115 | France 2007 |
| 63 | drill collar Ø178mm. | metre | 170 | France 2007 |
| 64 | Set of pony heavyweight drillpipe Ø127mm., G-105 х 9,19 length 3m., 5m., 7m., | set | 1 | France |